## Slide 1: Endoscopic Ultrasound Primer for Endoscopy Nurses
R.A.Singh MD FRCPC AGAF
Clinical Assistant Professor. Division of Gastroenterology, UBC

## Slide 2: Disclosures
Speaker Honorarium: Takeda
Abbvie
Janssen
Pentax
Clinical Research Takeda
Gilead
Celgene
Janssen

## Slide 3: Disclosures
Grants from Canadian Association of Gastroenterology, Royal College of Physician and Surgeons and Pentax for EUS training

## Slide 4: Agenda
Basics of EUS
Diagnostic Uses of EUS
Therapeutic Uses of EUS
Practical Nursing Advice
Questions

## Slide 5: “ Polar bear in a snow storm”

## Slide 6: Basics
Ultrasound image produced by US waves which are reflected back to the transducer as echoes
Reflection occurs due to acoustic impedence
A large difference of acoustic impedence between two tissues leads to greater reflection and poor transmission

## Slide 7: Ultrasound Mechanics

## Slide 8: U/S Mechanics

## Slide 9: Basics
Echoendoscope is an endoscope with an ultrasound transducer at the tip
Radial or linear ultrasound devices available
Standard EUS transducers operate from 7.5-12 MHz
Higher the frequency,lower the penetration
Linear array scopes allow FNA by real time visualization of the biopsy needle

## Slide 12: Basics
Acoustic coupling is achieved by a water filled balloon at the tip of the echoendoscope
EUS poor at delineating air filled structures or bone ( eg anterior mediastinum)
Artifacts occur as in abdominal US

## Slide 13: EUS Imaging
Anechoic
Hypoechoic
Hyperechoic

## Slide 14: Basics
Standard echoendoscopes image five layers of the gastrointestinal wall:
Superficial mucosa ( hyperechoic)
Deep mucosa ( hypoechoic)
Submucosa ( hyperechoic)
Muscularis propria ( hypoechoic)
Serosa (hyperechoic)

## Slide 18: Why do we need EUS?: Diagnostics
Improved diagnostic accuracy in staging a variety of tumours
Esophageal, gastric, pancreatic/biliary, rectal and NSCLC
Benign lesions such as sub-epithelial lesions, chronic pancreatitis and CBD stones best evaluated by EUS
Tissue acquisition

## Slide 19: Why do we need EUS?: Therapeutics
Celiac Plexus Blockade or Neurolysis
Pseudocyst or Necrosis Drainage
Biliary Access
Future needs include local chemotherapy and RFA (radiofrequency ablation)

## Slide 20: Basics: Tumor Staging
TNM classification is used to stage tumors with EUS:
T1 Extension into mucosa/submucosa
T2 Extension into but not beyond layer 4
T3 Spread beyond layer 4 but not surrounding structures
T4 Invasion of surrounding structures or vessels
Nodal staging are specific to type of tumors

## Slide 21: Esophageal T1 Lesion

## Slide 22: Esophageal T2 Lesion

## Slide 23: Esophageal T3 Lesion

## Slide 24: Esophageal T4 Lesion

## Slide 25: Tumour Staging: Nodes
Malignant nodes : Large (>1cm)
Homogeneous
Well Circumscribed
Round
If all 4 criteria are met , the specificity is high
FNA greatly increases the specificity

## Slide 26: Malignant Lymph Nodes

## Slide 27: Upper GI Tract: Benign Lesions
Sub-epithelial lesions:
Thickened Mucosal Folds
Lipomas
Carcinoid tumours
Varices
Pancreatic rests
Stromal lesions
Extrinsic Compression
( Tumours, Pseudocyst, Lymph nodes)

## Slide 28: GIST ( Gastrointestinal Stromal Tumour)

## Slide 29: Lipoma

## Slide 30: Gastric/Esophageal Varices

## Slide 31: Chronic Pancreatitis
Most sensitive radiographic modality for diagnosing chronic pancreatitis
Standard EUS criteria for diagnosing CP
Features include parenchymal calcification, lobulation, dilated tortuous PD

## Slide 32: Normal Pancreas

## Slide 33: Chronic Pancreatitis

## Slide 35: Choledocholithiasis
Most sensitive imaging technique for detecting stones
More sensitive than MRCP
Spatial resolution to 0.1mm ( sludge)
Increasingly used to rule out small stones in CBD

## Slide 38: Interventional EUS
EUS guided FNA
Celiac plexus neurolysis for CP or pancreatic cancer pain. Safer approach than traditional posterior fluoroscopically directed approach
Other indications include Drainage of pseudocysts, BOTOX injections for achalasia

## Slide 39: Pancreatic Pseudocyst

## Slide 40: Pseudocyst Drainage (Endoscopic)

## Slide 41: Pseudocyst (Endoscopic Drainage)

## Slide 42: Complications of EUS
Oxygen desaturation
Cardiac arrythmias
Perforation
Bleeding ( FNA)
Pancreatitis ( FNA)
Infection ( Local or Systemic)

## Slide 43: Antibiotic Prophylaxis
Cyst Aspiration
Rectal Lesion Puncture
Radial EUS exam is a low risk procedure
EUS/FNA should be considered a high risk procedure based on ASGE endocarditis guidelines

## Slide 44: Summary
EUS allows for accurate diagnosis of submucosal lesions
Greater accuracy in staging esophageal,gastric, pancreatic/ampullary and rectal carcinoma
Non invasive diagnostic modality for choledocholithiasis and chronic pancreatitis
EUS guide FNA allows for tissue sampling
Therapeutic EUS continues to evolve